## Slide 1: Introduction to Computer Architecture

## Slide 2: What is Computer Organization and Computer Architecture?
Computer Organization is concerned with the way hardware components operate and the way they are connected together to form the computer system.
Computer Architecture is concerned with the structure and behavior of the computer seen by the user.
It includes the information, formats, the instruction set and techniques for addressing memory.

## Slide 3: What is Computer Design?
Computer design is concerned with the hardware design of the computer.
With the formulated computer specifications, a designer has to develop hardware for the system.

## Slide 4: Overview of Unit - 1
This unit deals with the physical organization of a particular computer.
It includes the data flow, the micro operations and control functions.
These all can be described symbolically by means of a hardware description language.
The pre-requisite to understand all the concepts of computer architecture is the better understanding of Digital Electronics.

## Slide 5: Overview (contd…)
One part of the unit introduces the register transfer language (RTL).
This will explain how to introduce the micro-operations in the symbolic form.
Here, symbols are defined for arithmetic, logic and shift micro-operations.
On the completion of the unit, the student will be able to design a composite arithmetic logic shift unit.

## Slide 6: Overview (contd…)
The other part deals with the organization and design of a basic digital computer.
The Register Transfer Language (RTL) is used to describe the internal operation of the computer and to specify the requirements for its design.
This introduces the set of instructions used by the basic computer.

## Slide 7: Overview (contd…)
In short, this unit presents the detailed steps of the hardware organization and design.
Going through this unit will make you able to understand to understand the inner workings of digital computers.

## Slide 8: Preview of the Unit - 1
Register transfer
Micro-operation(Arithmetic, Logical and Shift)
Bus and Memory Transfer
Computer Registers
Computer Instructions
Timing and Control Unit
Instruction Cycle
Types of Instructions (Reg. Ref. , Mem. Ref. and IO Ref.)
Interrupt Cycle

## Slide 9: Lecture-2
Register Transfer

## Slide 10: Microoperations
The operations on the data in registers are called micro operations.
The functions built into registers are examples of micro operations
  Shift
  Load
  Clear
  Increment
  …

## Slide 11: Organization Of A Digital System
- Set of registers and their functions
- Micro-operations set
Set of allowable microoperations provided
by the organization of the computer
- Control signals that initiate the sequence of
microoperations (to perform the functions)
Definition of the (internal) organization of a computer

## Slide 12: Register Transfer Level
Viewing a computer, or any digital system, in this way is called the register transfer level
This is because we’re focusing on
  The system’s registers
  The data transformations in them, and
  The data transfers between them.

## Slide 13: Register Transfer Language
Rather than specifying a digital system in words, a specific notation is used, register transfer language
For any function of the computer, the register transfer language can be used to describe the (sequence of) microoperations
Register transfer language
  A symbolic language
  A convenient tool for describing the internal organization of digital computers
  Can also be used to facilitate the design process of digital systems.

## Slide 14: Designation Of Registers
Registers are designated by capital letters, sometimes followed by numbers (e.g., A, R13, IR)
Often the names indicate function:
  MAR - memory address register
  PC - program counter
  IR - instruction register
Registers and their contents can be viewed and represented in various ways
  A register can be viewed as a single entity:
  Registers may also be represented showing the bits of data they contain

## Slide 15: Designation Of Registers
R1
Register
Numbering of bits
Showing individual bits
Subfields
PC(H)
PC(L)
15
8
7
0
- a register
- portion of a register
- a bit of a register
Common ways of drawing the block diagram of a register
7 6 5 4 3 2 1 0
R2
15
0
Designation of a register

## Slide 16: Register Transfer
Copying the contents of one register to another is a register transfer
A register transfer is indicated as : R1 ← R2
  In this case the contents of register R2 are copied (loaded) into register R1
  A simultaneous transfer of all bits from the source R2 to the destination register R1, during one clock pulse
  Note that this is a non-destructive; i.e. the contents of R2 are not altered by copying (loading) them to R1

## Slide 17: Register Transfer
A register transfer such as R3  R5 implies that the digital system has
  the data lines from the source register (R5) to the destination register (R3)
  Parallel load in the destination register (R3)
  Control lines to perform the action

## Slide 18: Control Functions
Often actions need to only occur if a certain condition is true
This is similar to an “if” statement in a programming language
In digital systems, this is often done via a control signal, called a control function
  If the signal is 1, the action takes place
This is represented as- P: R2 ← R1
  Which means “if P = 1, then load the contents of register R1 into register R2”,
  i.e., if (P = 1) then (R2  R1)

## Slide 19: Hardware Implementation Of Controlled Transfers
Implementation of controlled transfer
P: R2 R1
Block diagram
Timing diagram
Clock
Transfer occurs here
R2
R1
Control
Circuit
Load
P
n
Clock
Load
t
t+1
The same clock controls the circuits that generate the control function
and the destination register
Registers are assumed to use positive-edge-triggered flip-flops

## Slide 20: Simultaneous Operations
If two or more operations are to occur simultaneously, they are separated with commas
  P: R3  R5, MAR  IR
Here, if the control function P = 1, load the contents of R5 into R3, and at the same time (clock), load the contents of register IR into register MAR

## Slide 21: Basic Symbols For Register Transfers
Capital letters Denotes a register MAR, R2
& numerals
Parentheses () Denotes a part of a register R2(0-7), R2(L)
Arrow  Denotes transfer of information R2  R1
Colon : Denotes termination of control function P:
Comma , Separates two micro-operations A  B, B  A
Symbols
Description Examples

## Slide 22: Connecting Registers
In a digital system with many registers, it is impractical to have data and control lines to directly allow each register to be loaded with the contents of every possible other registers
To completely connect n registers  n(n-1) lines
O(n2) cost
  This is not a realistic approach to use in a large digital system
Instead, take a different approach i.e., have one centralized set of circuits for data transfer – bus
Have control circuits to select which register is the source, and which is the destination

## Slide 23: Summary Of Register Transfer Microoperations
A  B Transfer content of reg. B into reg. A
AR DR(AD) Transfer content of AD portion of reg. DR into reg. AR
A  constant Transfer a binary constant into reg. A
ABUS  R1, Transfer content of R1 into bus A and, at the same time,
R2 ABUS transfer content of bus A into R2
AR Address register
DR Data register
M[R] Memory word specified by reg. R
M Equivalent to M[AR]
DR  M Memory read operation: transfers content of
memory word specified by AR into DR
M  DR Memory write operation: transfers content of
DR into memory word specified by AR

## Slide 24: Lecture-3
Bus and Memory Transfer

## Slide 25: Bus And Bus Transfer
Bus is a path (of a group of wires) over which information is transferred, from any of several sources to any of several destinations.
From a register to bus: BUS  R
Register A
Register B
Register C
Register D
Bus lines

## Slide 26
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
Register A
Register B
Register C
Register D
B
C
D
1
1
1
4 x1
MUX
B
C
D
2
2
2
4 x1
MUX
B
C
D
3
3
3
4 x1
MUX
B
C
D
4
4
4
4 x1
MUX
4-line bus
x
y
select
0
0
0
0

## Slide 27: Transfer From Bus To A Destination Register
Three-State Bus Buffers
Bus line with three-state buffers
Reg. R0
Reg. R1
Reg. R2
Reg. R3
Bus lines
2 x 4
Decoder
Load
D
0
D
1
D
2
D
3
z
w
Select
E (enable)
Output Y=A if C=1
High-impedence if C=0
Normal input A
Control input C
Select
Enable
0
1
2
3
S0
S1
A0
B0
C0
D0
Bus line for bit 0

## Slide 28: Bus Transfer In RTL
Depending on whether the bus is to be mentioned explicitly or not, register transfer can be indicated as either
or
In the former case the bus is implicit, but in the latter, it is explicitly indicated
R2  R1
BUS  R1, R2  BUS

## Slide 29: Memory (RAM)
Memory (RAM) can be thought as a sequential circuits containing some number of registers
These registers hold the words of memory
Each of the r registers is indicated by an address range from 0 to r-1and each register (word) can hold n bits of data
Assume the RAM contains r = 2k words. It needs the following
  n data input lines
  n data output lines
  k address lines
  A Read control line
  A Write control line
data input lines
data output lines
n
n
k
address lines
Read
Write
RAM
unit

## Slide 30: Memory Transfer
Collectively, the memory is viewed at the register level as a device, M.
We must specify which address in memory we will be using and it is done by indexing memory references
Memory is usually accessed in computer systems by putting the desired address in a special register, the Memory Address Register (MAR, or AR)
When memory is accessed, the contents of the MAR get sent to the memory unit’s address lines
AR
Memory
unit
Read
Write
Data in
Data out
M

## Slide 31: Memory Read
To read a value from a location in memory and load it into a register, the register transfer language notation looks like this:R1←M[MAR]
This causes the following to occur
  The contents of the MAR get sent to the memory address lines
  A Read (= 1) gets sent to the memory unit
  The contents of the specified address are put on the memory’s output data lines
  These get sent over the bus to be loaded into register R1

## Slide 32: Memory Write
To write a value from a register to a location in memory looks like this in register transfer language: R1←M[MAR]
This causes the following to occur
  The contents of the MAR get sent to the memory address lines
  A Write (= 1) gets sent to the memory unit
  The values in register R1 get sent over the bus to the data input lines of the memory
  The values get loaded into the specified address in the memory

## Slide 33: Lecture - 4
Arithmetic Micro-operations

## Slide 34: Bus Transfer
Common Bus: It is a structure that consists of a set of common lines , one for each bit of a register, through which binary information is transferred one at a time.
For e.g. If we have four registers and size of each register is of 4-bit.

## Slide 35: How to design a common bus? (in general)
Problem : Design a n-line common bus system that will multiplex ‘k’ registers of ‘n’ – bits each.
Solution :
No. of multiplexers required = n
Size of multiplexers=k X 1
No. of data lines = k
No. of select lines = m such that 2m = k

## Slide 36: Memory Transfer
Read: Transfer of information from a memory word to the outside environment.
Write : Transfer of new information to be stored into the memory.
Read: DR ← M[AR]
Write: M[AR] ← R1

## Slide 37: Microoperations
Computer system microoperations are of four types:
- Register transfer microoperations
- Arithmetic microoperations
- Logic microoperations
- Shift microoperations

## Slide 38: Arithmetic Micro operations
The basic arithmetic micro operations are
  Addition
  Subtraction
  Increment
  Decrement
The additional arithmetic micro operations are
  Add with carry
  Subtract with borrow
  Transfer/Load
  etc. …

## Slide 39: Summary of Typical Arithmetic Micro operations
  R3  R1 + R2 [Contents of R1 plus R2 transferred to R3]
  R3  R1 - R2 [Contents of R1 minus R2 transferred to R3]
  R2  R2’ [Complement the contents of R2 ]
  R2  R2’+ 1 [2's complement the contents of R2 (negate)]
  R3  R1 + R2’+ 1 [Subtraction]
  R1  R1 + 1 [Increment]
  R1  R1 - 1 [Decrement]

## Slide 40: Binary Adder

## Slide 41: Binary Adder-Subtractor

## Slide 42: Binary Incrementer

## Slide 43: Arithmetic Circuit Function Table
S1 S0 Cin Y Output Micro operation
0 0 0 B D = A + B Add
0 0 1 B D = A + B + 1 Add with carry
0 1 0 B’ D = A + B’ Subtract with borrow
0 1 1 B’ D = A + B’+ 1 Subtract
1 0 0 0 D = A Transfer A
1 0 1 0 D = A + 1 Increment A
1 1 0 1 D = A - 1 Decrement A
1 1 1 1 D = A Transfer A

## Slide 45: Lecture - 5
Logic Micro-operations and their Applications

## Slide 46: Logic Microoperations
Specify binary operations on the strings of bits in registers
  Logic micro operations are bit-wise operations, i.e., they work on the individual bits of data
  useful for bit manipulations on binary data
  useful for making logical decisions based on the bit value
0 0 0 0 0 … 1 1 1
0 1 0 0 0 … 1 1 1
1 0 0 0 1 … 0 1 1
1 1 0 1 0 … 1 0 1
A B F0 F1 F2 … F13 F14 F15

## Slide 47: List Of Logic Microoperations
Truth tables for 16 functions of 2 variables and the
corresponding 16 logic micro-operations
Boolean
Function
Micro-
Operations
Name
  0 0 0 0 F0 = 0 F  0 Clear
  0 0 0 1 F1 = xy F  A  B AND
  0 0 1 0 F2 = xy' F  A  B’
  0 0 1 1 F3 = x F  A Transfer A
  0 1 0 0 F4 = x'y F  A’ B
  0 1 0 1 F5 = y F  B Transfer B
  0 1 1 0 F6 = x  y F  A  B Exclusive-OR
  0 1 1 1 F7 = x + y F  A  B OR
  1 0 0 0 F8 = (x + y)' F  A  B)’ NOR
  1 0 0 1 F9 = (x  y)' F  (A  B)’ Exclusive-NOR
  1 0 1 0 F10 = y' F  B’ Complement B
  1 0 1 1 F11 = x + y' F  A  B
  1 1 0 0 F12 = x' F  A’ Complement A
  1 1 0 1 F13 = x' + y F  A’ B
  1 1 1 0 F14 = (xy)' F  (A  B)’ NAND
  1 1 1 1 F15 = 1 F  all 1's Set to all 1's

## Slide 48: Hardware Implementation Of Logic Micro operations
0 0 F = A  B AND
0 1 F = AB OR
1 0 F = A  B XOR
1 1 F = A’ Complement
S1 S0
Output
-operation
Function table
B
A
S
S
F
1
0
i
i
i
0
1
2
3
4 X 1
MUX
Select

## Slide 49: Applications Of Logic Micro operations
Logic micro operations can be used to manipulate individual bits or a portions of a word in a register
Consider the data in a register A. In another register, B, is bit data that will be used to modify the contents of A
  Selective-set A  A + B
  Selective-complement A  A  B
  Selective-clear A  A • B’
  Mask (Delete) A  A • B
  Clear A  A  B
  Insert  (A • B) + C
  Compare A  A  B

## Slide 50: Selective Set
In a selective set operation, the bit pattern in B is used to set certain bits in A
1 1 0 0 At
1 0 1 0 B
1 1 1 0 At+1 (A  A + B)
If a bit in B is set to 1, that same position in A gets set to 1, otherwise that bit in A keeps its previous value

## Slide 51: Selective Complement
In a selective complement operation, the bit pattern in B is used to complement certain bits in A
1 1 0 0 At
1 0 1 0 B
0 1 1 0 At+1 (A  A  B)
If a bit in B is set to 1, that same position in A gets complemented from its original value, otherwise it is unchanged

## Slide 52: Selective Clear
In a selective clear operation, the bit pattern in B is used to clear certain bits in A
1 1 0 0 At
1 0 1 0 B
0 1 0 0 At+1 (A  A  B’)
If a bit in B is set to 1, that same position in A gets set to 0, otherwise it is unchanged

## Slide 53: Mask Operation
In a mask operation, the bit pattern in B is used to clear certain bits in A
1 1 0 0 At
1 0 1 0 B
1 0 0 0 At+1 (A  A  B)
If a bit in B is set to 0, that same position in A gets set to 0, otherwise it is unchanged

## Slide 54: Clear Operation
In a clear operation, if the bits in the same position in A and B are the same, they are cleared in A, otherwise they are set in A
1 1 0 0 At
1 0 1 0 B
0 1 1 0 At+1 (A  A  B)

## Slide 55: Insert Operation
An insert operation is used to introduce a specific bit pattern into A register, leaving the other bit positions unchanged
This is done as
  A mask operation to clear the desired bit positions, followed by an OR operation to introduce the new bits into the desired positions
  Example: Suppose you wanted to introduce 1010 into the low order four bits of A:1101 1000 1011 0001A (Original) 1101 1000 1011 1010A (Desired)
  Solution: Mask original A with 1111 1111 1111 0000, then add 0000 0000 0000 1010 to intermediate result and we get the desired result.

## Slide 56: Lecture - 5
Logic Micro-operations and their Applications

## Slide 57: Logic Microoperations
Specify binary operations on the strings of bits in registers
  Logic micro operations are bit-wise operations, i.e., they work on the individual bits of data
  useful for bit manipulations on binary data
  useful for making logical decisions based on the bit value
0 0 0 0 0 … 1 1 1
0 1 0 0 0 … 1 1 1
1 0 0 0 1 … 0 1 1
1 1 0 1 0 … 1 0 1
A B F0 F1 F2 … F13 F14 F15

## Slide 58: List Of Logic Microoperations
Truth tables for 16 functions of 2 variables and the
corresponding 16 logic micro-operations
Boolean
Function
Micro-
Operations
Name
  0 0 0 0 F0 = 0 F  0 Clear
  0 0 0 1 F1 = xy F  A  B AND
  0 0 1 0 F2 = xy' F  A  B’
  0 0 1 1 F3 = x F  A Transfer A
  0 1 0 0 F4 = x'y F  A’ B
  0 1 0 1 F5 = y F  B Transfer B
  0 1 1 0 F6 = x  y F  A  B Exclusive-OR
  0 1 1 1 F7 = x + y F  A  B OR
  1 0 0 0 F8 = (x + y)' F  A  B)’ NOR
  1 0 0 1 F9 = (x  y)' F  (A  B)’ Exclusive-NOR
  1 0 1 0 F10 = y' F  B’ Complement B
  1 0 1 1 F11 = x + y' F  A  B
  1 1 0 0 F12 = x' F  A’ Complement A
  1 1 0 1 F13 = x' + y F  A’ B
  1 1 1 0 F14 = (xy)' F  (A  B)’ NAND
  1 1 1 1 F15 = 1 F  all 1's Set to all 1's

## Slide 59: Hardware Implementation Of Logic Micro operations
0 0 F = A  B AND
0 1 F = AB OR
1 0 F = A  B XOR
1 1 F = A’ Complement
S1 S0
Output
-operation
Function table
B
A
S
S
F
1
0
i
i
i
0
1
2
3
4 X 1
MUX
Select

## Slide 60: Applications Of Logic Micro operations
Logic micro operations can be used to manipulate individual bits or a portions of a word in a register
Consider the data in a register A. In another register, B, is bit data that will be used to modify the contents of A
  Selective-set A  A + B
  Selective-complement A  A  B
  Selective-clear A  A • B’
  Mask (Delete) A  A • B
  Clear A  A  B
  Insert  (A • B) + C
  Compare A  A  B

## Slide 61: Selective Set
In a selective set operation, the bit pattern in B is used to set certain bits in A
1 1 0 0 At
1 0 1 0 B
1 1 1 0 At+1 (A  A + B)
If a bit in B is set to 1, that same position in A gets set to 1, otherwise that bit in A keeps its previous value

## Slide 62: Selective Complement
In a selective complement operation, the bit pattern in B is used to complement certain bits in A
1 1 0 0 At
1 0 1 0 B
0 1 1 0 At+1 (A  A  B)
If a bit in B is set to 1, that same position in A gets complemented from its original value, otherwise it is unchanged

## Slide 63: Selective Clear
In a selective clear operation, the bit pattern in B is used to clear certain bits in A
1 1 0 0 At
1 0 1 0 B
0 1 0 0 At+1 (A  A  B’)
If a bit in B is set to 1, that same position in A gets set to 0, otherwise it is unchanged

## Slide 64: Mask Operation
In a mask operation, the bit pattern in B is used to clear certain bits in A
1 1 0 0 At
1 0 1 0 B
1 0 0 0 At+1 (A  A  B)
If a bit in B is set to 0, that same position in A gets set to 0, otherwise it is unchanged

## Slide 65: Clear Operation
In a clear operation, if the bits in the same position in A and B are the same, they are cleared in A, otherwise they are set in A
1 1 0 0 At
1 0 1 0 B
0 1 1 0 At+1 (A  A  B)

## Slide 66: Insert Operation
An insert operation is used to introduce a specific bit pattern into A register, leaving the other bit positions unchanged
This is done as
  A mask operation to clear the desired bit positions, followed by an OR operation to introduce the new bits into the desired positions
  Example: Suppose you wanted to introduce 1010 into the low order four bits of A:1101 1000 1011 0001A (Original) 1101 1000 1011 1010A (Desired)
  Solution: Mask original A with 1111 1111 1111 0000, then add 0000 0000 0000 1010 to intermediate result and we get the desired result.

## Slide 67: Lecture -7
Basic Computer Organization

## Slide 68: Introduction
Every different processor type has its own design (different registers, buses, micro operations, machine instructions, etc)
It contains
  Many registers
  Multiple arithmetic units, for both integer and floating point calculations
  The ability to pipeline several consecutive instructions to speed execution
We will use basic computer model to introduce processor organization and the relationship of the RTL model to the higher level computer processor

## Slide 69: The Basic Computer
The Basic Computer has two components, a processor and memory
The memory has 4096 words in it
  4096 = 212, so it takes 12 bits to select a word in memory
Each word is 16 bits long
CPU
RAM
0
4095
0
15

## Slide 70: Instructions
Program
  A sequence of (machine) instructions
(Machine) Instruction
  A group of bits that tell the computer to perform a specific operation (a sequence of micro-operation)
The instructions of a program, along with any needed data are stored in memory
The CPU reads the next instruction from memory
It is placed in an Instruction Register (IR)
Control circuitry in control unit then translates the instruction into the sequence of micro operations necessary to implement it

## Slide 71: Instruction Format
A computer instruction is often divided into two parts
  An opcode (Operation Code) that specifies the operation for that instruction
  An address that specifies the registers and/or locations in memory to use for that operation
In the Basic Computer, since the memory contains 4096 (= 212) words, we needs 12 bit to specify which memory address this instruction will use
In the Basic Computer, bit 15 of the instruction specifies the addressing mode (0: direct addressing, 1: indirect addressing)
Since the memory words, and hence the instructions, are 16 bits long, that leaves 3 bits for the instruction’s opcode

## Slide 72: Addressing Modes
The address field of an instruction can represent in two broad ways.
  Direct address: the address in memory of the data to use (the address of the operand).
  Indirect address: the address in memory of the address in memory of the data to use.
There are many more addressing modes as well.

## Slide 73: Addressing Modes (contd…)
0
ADD
457
22
Operand
457
1
ADD
300
35
1350
300
Operand
1350
+
AC
+
AC
Direct addressing
Indirect addressing

## Slide 74: Lecture-8
Basic Computer Registers

## Slide 75: Basic Computer Registers
Registers in the Basic Computer
11
0
PC
15
0
IR
15
0
TR
7
0
OUTR
15
0
DR
15
0
AC
11
0
AR
INPR
0
7
Memory
4096 x 16
CPU

## Slide 76: Basic Computer Registers (contd…)
  DR 16 Data Register Holds memory operand
  AR 12 Address Register Holds address for memory
  AC 16 Accumulator Processor register
  IR 16 Instruction Register Holds instruction code
  PC 12 Program Counter Holds address of instruction
  TR 16 Temporary Register Holds temporary data
  INPR 8 Input Register Holds input character
  OUTR 8 Output Register Holds output character

## Slide 77: Processor Registers
A processor has many registers to hold instructions, addresses, data, etc
The processor has a register, the Program Counter (PC) that holds the memory address of the next instruction to get
  Since the memory in the Basic Computer only has 4096 locations, the PC only needs 12 bits
The Address Register (AR) is a 12 bit register in the Basic Computer to hold the memory address
When an operand is found, using either direct or indirect addressing, it is placed in the Data Register (DR). The processor then uses this value as data for its operation
The Basic Computer has a single general purpose register – the Accumulator (AC)

## Slide 78
The significance of a general purpose register is that it can be referred to in instructions
  e.g. load AC with the contents of a specific memory location; store the contents of AC into a specified memory location
Often a processor will need a scratch register to store intermediate results or other temporary data; in the Basic Computer this is the Temporary Register (TR)
The Input Register (INPR) holds an 8 bit character received from an input device
The Output Register (OUTR) holds an 8 bit character to be send to an output device

## Slide 79: Common Bus System
The registers in the Basic Computer are connected using a bus
This gives a savings in circuitry over complete connections between registers

## Slide 80: Common Bus System
S2
S1
S0
Bus
Memory unit
4096 x 16
LD INR CLR
Address
Read
Write
AR
LD INR CLR
PC
LD INR CLR
DR
LD INR CLR
AC
ALU
E
INPR
IR
LD
LD INR CLR
TR
OUTR
LD
Clock
16-bit common bus
7
1
2
3
4
5
6

## Slide 81: Common Bus System
AR
PC
DR
L
I
C
L
I
C
L
I
C
AC
L
I
C
ALU
E
IR
L
TR
L
I
C
OUTR
LD
INPR
Memory
4096 x 16
Address
Read
Write
16-bit Common Bus
7
1
2
3
4
5
6
S0
S1
S2

## Slide 82: Common Bus System
Three control lines, S2, S1, and S0 control which register the bus selects as its input
Either one of the registers will have its load signal activated, or the memory will have its read signal activated
  Will determine where the data from the bus gets loaded
The 12-bit registers, AR and PC, have 0’s loaded onto the bus in the high order 4 bit positions
When the 8-bit register OUTR is loaded from the bus, the data comes from the low order 8 bits on the bus

## Slide 83: Lecture-9 & 10
Computer Instructions and Timing and Control Unit

## Slide 84: Basic Computer Instructions
Basic Computer Instruction Format
15 14
12 11
0
I
Opcode
Address
Memory-Reference Instructions (OP-code = 000 ~ 110)
Register-Reference Instructions (OP-code = 111, I = 0)
Input-Output Instructions (OP-code =111, I = 1)
15
12 11
0
Register operation
0 1 1 1
15
12 11
0
I/O operation
1 1 1 1

## Slide 85: Basic Computer Instructions
Hex Code
Symbol I = 0 I = 1 Description
  AND 0xxx 8xxx AND memory word to AC
  ADD 1xxx 9xxx Add memory word to AC
  LDA 2xxx Axxx Load AC from memory
  STA 3xxx Bxxx Store content of AC into memory
  BUN 4xxx Cxxx Branch unconditionally
  BSA 5xxx Dxxx Branch and save return address
  ISZ 6xxx Exxx Increment and skip if zero
  CLA 7800 Clear AC
  CLE 7400 Clear E
  CMA 7200 Complement AC
  CME 7100 Complement E
  CIR 7080 Circulate right AC and E
  CIL 7040 Circulate left AC and E
  INC 7020 Increment AC
  SPA 7010 Skip next instr. if AC is positive
  SNA 7008 Skip next instr. if AC is negative
  SZA 7004 Skip next instr. if AC is zero
  SZE 7002 Skip next instr. if E is zero
  HLT 7001 Halt computer
  INP F800 Input character to AC
  OUT F400 Output character from AC
  SKI F200 Skip on input flag
  SKO F100 Skip on output flag
  ION F080 Interrupt on
  IOF F040 Interrupt off
85

## Slide 86: Instruction Set Completeness
Instruction Types
A computer should have a set of instructions so that the user can
construct machine language programs to evaluate any function that is known to be computable.
  Functional Instructions
  - Arithmetic, logic, and shift instructions
  (ADD, CMA, INC, CIR, CIL, AND, CLA)
  Transfer Instructions
  - Data transfers between the main memory
  and the processor registers (LDA, STA)
  Control Instructions
  - Program sequencing and control (BUN, BSA, ISZ)
  Input/Output Instructions
  - Input and output (INP, OUT)

## Slide 87: Timing And Control Unit
Control unit (CU) of a processor translates from machine instructions to the control signals for the micro operations that implement them.
Timing for all registers in the basic computer is controlled by a master clock.
Clock pulses donot change the state of a register unless the register is enabled by the control signal generated by CU.

## Slide 88: Types Of Control Unit
Control units are implemented in one of two ways:
1. Hardwired Control Unit
  CU is made up of sequential and combinational circuits to generate the control signals.
  Advantage: Can be optimized to produce fast mode of operation.
  Disadvantage: Requires changes in wiring, if the designed has to be modified.
2. Micro programmed Control Unit
  A control memory on the processor contains micro programs that activate the necessary control signals.
  Advantage: Any required changes can be done by updating the micro program.

## Slide 89: Hardwired Timing And Control Unit
Control unit of Basic Computer
Instruction register (IR)
15
14 13 12
11 - 0
3 x 8
decoder
7 6 5 4 3 2 1 0
I
D
0
15 14 . . . . 2 1 0
4 x 16
decoder
4-bit
sequence
counter
(SC)
Increment (INR)
Clear (CLR)
Clock
Other inputs
Control
signals
D
T
T
7
15
0
Combinational
Control
logic

## Slide 90: Timing Signals
- Generated by 4-bit sequence counter and 416 decoder
- The SC can be incremented or cleared.
- Example: T0, T1, T2, T3, T4, T0, T1, . . .
Assume: At time T4, SC is cleared to 0 if decoder output D3 is active i.e., D3T4: SC 0

## Slide 91: Lecture-11
Instruction Cycle and Register-Reference Instructions

## Slide 92: Instruction Cycle
In Basic Computer, a machine instruction is executed in the following cycle:
  Fetch an instruction from memory
  Decode the instruction
  Read the effective address from memory if the instruction has an indirect address
  Execute the instruction
After an instruction is executed, the cycle starts again at step 1, for the next instruction
Note: Every different processor has its own (different) instruction cycle

## Slide 93: Fetch And Decode
• Fetch and Decode
T0: AR PC (S0S1S2=010, T0=1)
T1: IR  M [AR], PC  PC + 1 (S0S1S2=111, T1=1)
T2: D0, . . . , D7  Decode IR(12-14), AR  IR(0-11), I  IR(15)
S2
S1
S0
Bus
7
Memory
unit
Address
Read
AR
LD
PC
INR
IR
LD
Clock
1
2
5
Common bus
T1
T0

## Slide 94: Determine The Type Of Instruction
= 0 (direct)
D'7IT3: AR M[AR] D'7I'T3: Nothing
D7I‘ T3: Execute a register-reference instr.
D7I T3: Execute an input-output instr.
Start
SC  0
AR

PC
T0
IR

M[AR],
PC

PC + 1
T1
AR

IR(0-11),
I

IR(15)
Decode Opcode in IR(12-14),
T2
D7
= 0 (Memory-reference)
(Register or I/O) = 1
I
I
Execute
register-reference
instruction
SC

0
Execute
input-output
instruction
SC

0
M[AR]

AR
Nothing
= 0 (register)
(I/O) = 1
(indirect) = 1
T3
T3
T3
T3
Execute
memory-reference
instruction
SC

0
T4

## Slide 95: Register Reference Instructions
r = D7 IT3 => Register Reference Instruction
Bi = IR(i) , i=0,1,2,...,11
- D7 = 1, I = 0
- Register Ref. Instr. is specified in b0 ~ b11 of IR
- Execution starts with timing signal T3
Register Reference Instructions are identified when
r: SC  0
CLA rB11: AC  0
CLE rB10: E  0
CMA rB9: AC  AC’
CME rB8: E  E’
CIR rB7: AC  shr AC, AC(15)  E, E  AC(0)
CIL rB6: AC  shl AC, AC(0)  E, E  AC(15)
INC rB5: AC  AC + 1
SPA rB4: if (AC(15) = 0) then (PC  PC+1)
SNA rB3: if (AC(15) = 1) then (PC  PC+1)
SZA rB2: if (AC = 0) then (PC  PC+1)
SZE rB1: if (E = 0) then (PC  PC+1)
HLT rB0: S  0 (S is a start-stop flip-flop)

## Slide 96: Lecture - 12
Memory Reference Instructions

## Slide 97: Memory Reference Instructions
Symbol
Operation
Decoder
Symbolic Description
AND D0 AC  AC  M[AR]
ADD D1 AC  AC + M[AR], E  Cout
LDA D2 AC  M[AR]
STA D3 M[AR]  AC
BUN D4 PC  AR
BSA D5 M[AR]  PC, PC  AR + 1
ISZ D6 M[AR]  M[AR] + 1, if M[AR] + 1 = 0 then PC  PC+1
The effective address of the instruction is in AR and was placed there during timing signal T2 when I = 0, or during timing signal T3 when I = 1
Memory cycle is assumed to be short enough to complete in a CPU cycle
The execution of MR instruction starts with T4

## Slide 98: Memory Reference Instruction
AND to AC
D0T4: DR  M[AR] Read operand
D0T5: AC  AC  DR, SC  0 AND with AC
ADD to AC
D1T4: DR  M[AR] Read operand
D1T5: AC  AC + DR, E  Cout, SC  0 Add to AC and store carry in E

## Slide 99: Memory Reference Instruction
LDA: Load to AC
D2T4: DR  M[AR]
D2T5: AC  DR, SC  0
STA: Store AC
D3T4: M[AR]  AC, SC  0
BUN: Branch Unconditionally
D4T4: PC  AR, SC  0

## Slide 100: Memory Reference Instruction
BUN instruction is an unconditional Jump instruction from one memory location to another memory location.
If we want to come back to the old memory location, then it will not be possible.
For that, there is another instruction i.e., BSA.

## Slide 101: Memory Reference Instructions
Memory, PC after execution
21
0
BSA
135
Next instruction
Subroutine
20
PC = 21
AR = 135
136
1
BUN
135
Memory, PC, AR at time T4
0
BSA
135
Next instruction
Subroutine
20
21
135
PC = 136
1
BUN
135
Memory
Memory
BSA: Branch and Save Return Address
D5T4: M[AR]  PC, PC  AR + 1
D5T5: PC  AR, SC  0

## Slide 102: Memory Reference Instructions
ISZ: Increment and Skip-if-Zero
D6T4: DR  M[AR]
D6T5: DR  DR + 1
D6T4: M[AR]  DR,
if (DR = 0) then (PC  PC + 1), SC  0

## Slide 103: FLOWCHART
Memory-reference instruction
DR  M[AR]
DR  M[AR]
DR  M[AR]
M[AR]  AC
SC  0
AND
ADD
LDA
STA
AC  AC DR
SC  0
AC  AC + DR
E  Cout
SC  0
AC  DR
SC  0
D T
0
4
D T
1
4
D T
2
4
D T
3
4
D T
0
5
D T
1
5
D T
2
5
PC  AR
SC  0
M[AR]  PC
AR  AR + 1
DR  M[AR]
BUN
BSA
ISZ
D T
4
4
D T
5
4
D T
6
4
DR  DR + 1
D T
5
5
D T
6
5
PC  AR
SC  0
M[AR]  DR
If (DR = 0)
then (PC  PC + 1)
SC  0
D T
6
6


## Slide 104: Lecture - 13
I/O Reference Instructions

## Slide 105
Input-Output Configuration
INPR Input register - 8 bits
OUTR Output register - 8 bits
FGI Input flag - 1 bit
FGO Output flag - 1 bit
IEN Interrupt enable - 1 bit
Input-output
terminal
Serial
communication
interface
Computer
registers and
flip-flops
Printer
Keyboard
Receiver
interface
Transmitter
interface
FGO
OUTR
AC
INPR
FGI
Serial Communications Path
Parallel Communications Path

## Slide 106: Input-Output And Interrupt
The terminal sends and receives serial information
The serial info. from the keyboard is shifted into INPR
The serial info. for the printer is stored in the OUTR
INPR and OUTR communicate with the terminal serially and with the AC in parallel.
The flags are needed to synchronize the timing difference between I/O device and the computer

## Slide 107: Input-Output Instructions
D7IT3 = p
IR(i) = Bi, i = 6, …, 11
p: SC  0 Clear SC
INP pB11: AC(0-7)  INPR, FGI  0 Input char. to AC
OUT pB10: OUTR  AC(0-7), FGO  0 Output char. from AC
SKI pB9: if(FGI = 1) then (PC  PC + 1) Skip on input flag
SKO pB8: if(FGO = 1) then (PC  PC + 1) Skip on output flag
ION pB7: IEN  1 Interrupt enable on
IOF pB6: IEN  0 Interrupt enable off

## Slide 108: Program-controlled Input/Output
Program-controlled I/O
- Continuous CPU involvement
I/O takes valuable CPU time
- CPU slowed down to I/O speed
- Simple
- Least hardware
I/O and Interrupt
Input
LOOP, SKI DEV
BUN LOOP
INP DEV
Output
LOOP, LDA DATA
LOP, SKO DEV
BUN LOP
OUT DEV

## Slide 109: Interrupt Initiated Input/Output
Open communication only when some data has to be passed --> interrupt.
The I/O interface, instead of the CPU, monitors the I/O device.
When the interface founds that the I/O device is ready for data transfer, it generates an interrupt request to the CPU
Upon detecting an interrupt, the CPU stops momentarily the task it is doing, branches to the service routine to process the data transfer, and then returns to the task it was performing.
IEN (Interrupt-enable flip-flop):
- can be set and cleared by instructions.
- when cleared, the computer cannot be interrupted

## Slide 110: Flowchart Of Interrupt Cycle
- The interrupt cycle is a HW implementation of a branch and save return address operation.
- At the beginning of the next instruction cycle, the
instruction that is read from memory is in address 1.
- At memory address 1, the programmer must store a branch instruction
that sends the control to an interrupt service routine
- The instruction that returns the control to the original
program is "indirect BUN 0"

## Slide 112: Lecture - 14
Design of Basic Computer

## Slide 113: Design of Basic Computer
Hardware Components of BC
A memory unit: 4096 x 16.
Registers:
AR, PC, DR, AC, IR, TR, OUTR, INPR, and SC
Flip-Flops(Status): I, S, E, R, IEN, FGI, and FGO
Decoders: A 3x8 Opcode decoder and A 4x16 timing decoder
Common bus: 16 bits
Control logic gates:
Adder and Logic circuit: Connected to AC

## Slide 114: contd…
Control Logic Gates
  Input Controls of the nine registers
  Read and Write Controls of memory
  Set, Clear, or Complement Controls of the flip-flops
  S2, S1, S0 Controls to select a register for the bus
  AC, and Adder and Logic circuit

## Slide 115: Control Of Registers And Memory
Scan all of the register transfer statements that change the content of AR:
R’T0: AR  PC LD(AR)
R’T2: AR  IR(0-11) LD(AR)
D’7IT3: AR  M[AR] LD(AR)
RT0: AR  0 CLR(AR)
D5T4: AR  AR + 1 INR(AR)

## Slide 116: contd…
AR
LD
INR
CLR
Clock
To bus
12
From bus
12
D'
I
T
T
R
T
D
T
7
3
2
0
4

## Slide 117: Control of Flags
pB7: IEN  1 (I/O Instruction)
pB6: IEN  0 (I/O Instruction)
RT2: IEN  0 (Interrupt)
p = D7IT3 (Input/Output Instruction)
D
I
T3
7
J
K
Q
IEN
p
B
7
B
6
T
2
R