## Slide 1: Memory Reference Instructions Session No.: Course Name: Computer Organisation and Architecture Course Code: RIUC305 T Duration: 50 MIN Date of Conduction of Class:

## Slide 2: Opening Activity (5 mins)
Quick Recall Quiz:
- What are the steps when CPU executes an instruction?
- Which step involves interaction with memory?

## Slide 3: At the end of this session students will be able to
Learning Outcome 1:1. Explain memory reference instructions in a basic computer.
Learning Outcome 2:2. Identify different types of memory reference instructions..
Learning Objectives

## Slide 4: Instruction Types
Categories of Instructions:
- Memory Reference Instructions
- Register Reference Instructions
- Input-Output Instructions
Focus: Memory Reference Instructions

## Slide 5: Memory Reference Instructions (Overview)
Operates on Accumulator (AC) and memory.
Require 12-bit address and 3-bit opcode.
Common in Basic Computer Model.

## Slide 6: List of Memory Reference Instructions
AND: AC ← AC ∧ M[addr]
ADD: AC ← AC + M[addr]
LDA: AC ← M[addr]
STA: M[addr] ← AC
BUN: PC ← addr
BSA: M[addr] ← PC; PC ← addr+1
ISZ: M[addr] ← M[addr]+1; if M[addr]=0 then PC←PC+1

## Slide 7: FLOWCHART
Memory-reference instruction
DR  M[AR]
DR  M[AR]
DR  M[AR]
M[AR]  AC
SC  0
AND
ADD
LDA
STA
AC  AC DR
SC  0
AC  AC + DR
E  Cout
SC  0
AC  DR
SC  0
D T
0
4
D T
1
4
D T
2
4
D T
3
4
D T
0
5
D T
1
5
D T
2
5
PC  AR
SC  0
M[AR]  PC
AR  AR + 1
DR  M[AR]
BUN
BSA
ISZ
D T
4
4
D T
5
4
D T
6
4
DR  DR + 1
D T
5
5
D T
6
5
PC  AR
SC  0
M[AR]  DR
If (DR = 0)
then (PC  PC + 1)
SC  0
D T
6
6


## Slide 8: Execution Examples
Example 1: ADD 500 → AC ← AC + M[500]
Example 2: STA 600 → M[600] ← AC
Show step-by-step fetch-decode-execute cycle.

## Slide 9: Active Learning 1 (Think-Pair-Share, 15 mins)
Instruction ISZ 450
Case 1: Memory[450] = -1
Case 2: Memory[450] = 0
Steps: Think (2 min) → Pair (5 min) → Share (8 min).

## Slide 10: Addressing Modes
- Direct Addressing
- Indirect Addressing
- Immediate Addressing (if supported)
Examples with instruction format.

## Slide 11: Control Flow Instructions
BUN, BSA, ISZ affect program flow.
Comparison with high-level constructs (loops, function calls).

## Slide 12: Active Learning 2 (Problem-Based Learning, 15 mins)
Problem: Write a sequence of instructions to add values at memory[500] and memory[501],
and store result at memory[502].
Steps: Individual (5 min) → Group discussion (5 min) → Share (5 min).

## Slide 13: Case Illustration
High-Level Code: C = A + B;
Equivalent Memory Reference Instructions:
LDA A
ADD B
STA C

## Slide 14: Summary
Types of memory reference instructions.
Execution steps.
Example problems.
Role in program execution and flow control.

## Slide 15: Reflection Activity (5 mins)
Questions:
- Which instruction was easiest and why?
- Which instruction was most confusing?
- How do low-level instructions connect to high-level programs?

## Slide 16: Closing & Next Lecture
Recap key takeaways.
Next: Register Reference & I/O Instructions.