## Slide 1: Register Reference Instructions Session No.: Course Name: Computer Organisation and Architecture Course Code: RIUC305 T Duration: 50 MIN Date of Conduction of Class:

## Slide 2: Opening Activity
Activity: How many CPU registers can you name in 60 seconds?
Encourage pair/group answers
Purpose: Refresh CPU basics, energize class, connect to topic

## Slide 3: At the end of this session students will be able to
Learning Outcome 1:1. Explain Register reference instructions in a basic computer.
Learning Outcome 2:2. You will be able to analyze why register reference instructions are more efficient compared to memory reference instructions for certain operations
Learning Objectives

## Slide 4: Instruction Classification Recap
Memory Reference Instructions
Input-Output Instructions
Register Reference Instructions (today’s focus)

## Slide 5: Definition
Executed when opcode = 111 (Basic Computer design)
Operate directly on CPU registers without memory access

## Slide 6: Instruction Format
16-bit instruction word
Bits 0–11: Operation field (register reference)
Bit 12: I (Indirect bit = 0 for register reference)
Bits 13–15: Opcode = 111

## Slide 7: Register Reference Instructions Examples
CLA: Clear AC
CLE: Clear E
CMA: Complement AC
CME: Complement E
CIR: Circulate right
CIL: Circulate left
INC: Increment AC
SPA: Skip if AC positive
SNA: Skip if AC negative
SZA: Skip if AC zero
SZE: Skip if E = 0
HLT: Halt execution

## Slide 8: Micro-operations Explanation
CLA: AC ← 0
INC: AC ← AC + 1
CIR: AC,E shifted right
CIL: AC,E shifted left

## Slide 9: Importance in CPU Design
Provides internal operations for CPU data manipulation
Used for testing, conditional control, and execution flow
Simplifies instruction set architecture

## Slide 10: Active Learning 1: Think-Pair-Share
Question: Why are register reference instructions useful?
Step 1: Think individually (2 min)
Step 2: Pair discussion (5 min)
Step 3: Share with class (8 min)
Instructor summarizes

## Slide 11: Example Problem: CIR Instruction
AC = 1010 0110, E = 1
After CIR execution → Shift right through E
Result inserted back into AC MSB

## Slide 12: Active Learning 2: Problem-Based Learning
Case: Program checks if AC=0; if yes, halt; else increment AC
Task: Design sequence of register reference instructions
Group discussion (10 min), presentation (5 min)

## Slide 13: Summary
Definition, format, opcode field
Examples (CLA, CMA, INC, CIR, HLT, etc.)
Role in CPU control and execution

## Slide 14: Reflection Activity: One-Minute Paper
Write one key learning from today’s lecture
Write one question you still have
Instructor collects responses for feedback

## Slide 15: Next Topic
Input Output Instructions